## Slide 1: Weekly Meeting 1
To do:
What is a Robot?
What is difference between Serial and Parallel robotic manipulator?
What are Forward and Inverse Kinematics of a robot?
Derive relationship of Forward and Inverse Kinematics of a 2 D.O.F. serial robot?
What are the main components of a serial robot?
What is the difference between revolute and translational joints?
What is an end effector of a robot?
What is DOF?

## Slide 2: What is a Robot?
“A robot is an autonomous machine capable of sensing its environment, carrying out computations to make decisions, and performing actions in the real world.”
A robot is a mechanical or virtual device that is designed to perform tasks autonomously or semi-autonomously. It can be programmed to execute specific actions, interact with its environment, and make decisions based on its sensors and programming.
Robots can come in various forms, ranging from industrial robotic arms used in manufacturing to humanoid robots and autonomous vehicles. They can be controlled by pre-programmed instructions, remote control, or through artificial intelligence algorithms.

## Slide 3: What is difference between Serial and Parallel robotic manipulator? The main difference between serial and parallel robotic manipulators lies in their structural design and the way they achieve motion.
Serial Manipulator: A serial manipulator, also known as a serial robot, is a type of robotic manipulator where the links or segments of the robot are connected in a linear chain, one after the other. This means that each joint of the robot is actuated independently, and the motion is transmitted serially from the base to the end effector. Serial manipulators are commonly used in industrial robotic arms. Examples include the popular 6-axis robotic arms found in manufacturing applications. Advantages of serial manipulators:
  Precise control over individual joints.
  More flexibility in terms of workspace and reach.
  Easier to program for a wide range of tasks.
  Generally simpler kinematics and control algorithms.
Parallel Manipulator: A parallel manipulator, as the name suggests, involves multiple kinematic chains or limbs that are connected in parallel. This means that the end effector is supported and moved by multiple actuators and linkages simultaneously. The actuators and linkages work together in a coordinated manner to control the motion of the end effector. Parallel manipulators are often used in applications where high precision, stiffness, or specific force distribution is required. Advantages of parallel manipulators:
  High rigidity and stiffness due to multiple actuators and linkages.
  Enhanced precision and accuracy in certain applications.
  Better force distribution capabilities.
  Faster response and dynamic performance.

## Slide 4: Pictures
Serial Manipulator
Parallel Manipulator

## Slide 5: In what category does a quadruped lie?
A quadruped typically falls under the category of a parallel manipulator. This is because a quadruped robot consists of multiple limbs (four legs in this case) that are connected in parallel. Each leg of the robot operates independently and contributes to the overall motion and control of the robot.
In a quadruped robot, the legs work in a coordinated manner to provide stability, locomotion, and manipulation capabilities. The parallel structure of the quadruped allows for better force distribution, stability, and the ability to perform dynamic movements.
It's worth noting that while a quadruped robot can be considered a parallel manipulator in terms of its structure, the specific implementation and design choices can vary. Some quadruped robots may have additional serial manipulators or mechanisms incorporated for specialized tasks or functionalities.